## Slide 1: rWHALE: Regional Workflow for Hazards and Loss Estimation
Wael Elhaddad
NHERI SimCenter
Programming Bootcamp 2019

## Slide 2: Outline
Overview of the Computational Framework
Regional Workflows using rWHALE
Regional Testbed Simulations
  San Francisco Testbed
  Anchorage Testbed
Demos & Exercises
  Local computer
  High performance computer (HPC)

## Slide 3: NHERI SimCenter
Data storage and HPC access
“Transforming the nation’s ability to understand and mitigate adverse effects of natural hazards on the built environment through computational simulation”
SimCenter Research Tools
Front-end
Cloud-enabled research tools, scalable to run on HPC
Emphasis on uncertainty quantification
Educational resources
SimCenter’s
Application Framework
Back-end
Notes: DesignSafe’s Agave interface allows access to their resources through web-based or cloud-based technologies.
The SimCenter leverage this cloud platform to develop desktop research applications that facilitates running large simulations on HPC. This requires the SimCenter to deploy its application framework(backend) on DesignSafe computing resources.

## Slide 4: Framework for Building Workflow Applications
Run in the cloud
OR
Run Locally
Notes: This slide explains the application framework and shows where research applications fall within this framework.

## Slide 5: Computations Workflow
Buildings Database
Hazard
Building Workflow
Regional workflow
Single building workflow
EVENT
BIM
SAM
EDP
DL
BIM: Building Information Model
SAM: Structural Analysis Model
EDP: Engineering Demand Parameters
DL: Damage & Loss
Buildings Database
Regional Simulation
Hazard
Damage &
Loss

## Slide 6: Workflow Overview
performUQ
Applications & Interfaces
BIM
Applications workflow
createBIM
EVENT
createEVENT
SAM
createSAM
EDP
createEDP
DL
createLOSS
BIM: Building Information Model
SAM: Structural Analysis Model
EDP: Engineering Demand Parameters
DL: Damage & Loss
lighter text are Inputs/Outputs
darker text are applications
Buildings Database
Files workflow (Interfaces)
performSIM
Obtain EDP

## Slide 7: Forward Uncertainty Propagation
Sample-1
pBIM: Parameterized BIM
pSAM: Parameterized SAM
Uncertainties are handled using Dakota
Each workflow application is called initially to define random variables
Dakota samples the random variables and runs the workflow applications for each sample
EVENT
BIM
SAM
EDP
DL
EVENT
pBIM
pSAM
performUQ i.e. Dakota
DL
Sample-N
EVENT
BIM
SAM
EDP
DL
Adams, B.M., Bauman, L.E., Bohnhoff, W.J., Dalbey, K.R., Ebeida, M.S., Eddy, J.P., Eldred, M.S., Hough, P.D., Hu, K.T., Jakeman, J.D., Stephens, J.A., Swiler, L.P., Vigil, D.M., and Wildey, T.M., "Dakota, A Multilevel Parallel Object-Oriented Framework for Design Optimization, Parameter Estimation, Uncertainty Quantification, and Sensitivity Analysis: Version 6.8 Theory Manual," Sandia Technical Report SAND2014-4253, May 2018.

## Slide 8: Registered Applications For Regional Earthquake Simulations
Type
Name
Description
createBIM
GenericBimDatabase
Creates a simple BIM from a building flat file (csv)
UrbanSimDatabase
Creates a simple BIM from
UrbanSim
simulation outputs
createEVENT
LLNL_SW4
Gets Event input from SW4
outputs
SHA
-
GM
Computes event input using SHA and record selection/scaling
createSAM
MDOF_LU
Creates a MDOF shear building model
createEDP
StandardEarthquakeEDP
Defines the standard EDPs used for a seismic event
performSIM
OpenSeesSimulation
Performs simulation using
OpenSees
and calculates the EDPs
createLOSS
FEMAP58_LU
Calculates damage and loss estimates using FEMA P-58 procedure
performUQ
DakotaFEM
Propagates uncertainty in all applications using Dakota

## Slide 9: Registered Applications For Regional Wind Simulations
Type
Name
Description
createBIM
GenericBimDatabase
Creates a simple BIM from a building flat file (csv)
UrbanSimDatabase
Creates a simple BIM from
UrbanSim
simulation outputs
createEVENT
ASCE 7-10
Generate wind loading using ASCE7-10 procedure
Stochastic Wind
Generate wind loading using stochastic process models
createSAM
MDOF_LU
Creates a MDOF shear building model
createEDP
StandardWindEDP
Defines the standard EDPs used for a wind event (e.g. pressure)
performSIM
OpenSeesSimulation
Performs simulation using
OpenSees
and calculates the EDPs
createLOSS
PELICUN(Hazus)
Calculates damage and loss estimates using Hazus methodology
performUQ
DakotaFEM
Propagates uncertainty in all applications using Dakota

## Slide 10: Regional Simulation Tools
San Francisco Bay Area Testbed
Hazard Consequences
Building Inventory
M7.0 Hayward

## Slide 11: Regional Simulation Tools
Regional simulation using HPC through DesignSafe Workspace

## Slide 12: Regional Simulation Tools
Small scale simulation using Local Computer
Applications,
Sample Data &
Examples
Runs Locally as a console application

## Slide 13: Regional Simulation Tools
The Framework provides applications with standard interfaces
LLNL_SW4
MDOF_LU
SHA-GM.py
Concrete Shear Walls
FEMA P58_LU
Multiple Fidelity Modeling
Pelicun
Buildings
Generic BIM
UrbanSIM
Document Database
Hazard
Modeling
Losses
NNGM.py
Seismic
Hazard
Analysis
Generic BIM
Simple Model
Hazus
Low Fidelity
High Fidelity
Seismic
Wave
Propagation
Detailed BIM
High Fidelity Model
FEMA P58
Earthquake
Simulation
Workflows

## Slide 14: Regional Simulation Configuration
Configuration File

## Slide 15: Regional Testbeds Using rWHALE
Memphis, TN Lifelines Testbed
Atlantic City, NJ Storm Testbed

## Slide 16: Example Simulation: Earthquake in San Francisco Bay Area
  M7.0 Rupture along the Hayward fault modeled using SW4 [1]
  1,843,351 buildings were included in the Simulation
  Building information is based on UrbanSim data
  Damage and Loss calculation using FEMAP58_LU [2]
  Structural analysis models are based on MDOF_LU [3]
  Red tagged buildings: 141,459
  Buildings damage: $84.1 billion
  Net buildings damage ratio: 5.6%
[1] A. J. Rodgers, A. Pitarka, N. A. Petersson, B. Sjögreen and D. B. McCallen, "Broadband (0–4 Hz) ground motions for a magnitude 7.0 Hayward fault earthquake with three‐dimensional structure and topography," Geophysical Research Letters, vol. 45, p. 739–747, 2018.
[2] Zeng X., Lu X.Z., Yang T., Xu Z., "Application of the FEMA-P58 methodology for regional earthquake loss prediction", Natural Hazards (2016), 10.1007/s11069-016-2307-z
[3] X. Lu, B. Han, M. Hori, C. Xiong and Z. Xu, "A coarse-grained parallel approach for seismic damage simulations of urban areas based on refined models and GPU/CPU cooperative computing," Advances in Engineering Software, vol. 70, pp. 90-103, 2014.
Building Loss Ratio

## Slide 17: Visualization
Visualization on parcel level results can be done in GIS tools (e.g. QGIS)
Loss Ratios
Red Tagged Buildings

## Slide 18: Parcel Level Results
Loss Ratios

## Slide 19: Comparison To HayWired Scenario
 | HayWired Scenario | SimCenter Testbed
Number of Buildings | 3 Million | 1.84 Million
Red Tagged Buildings | 101,000 | 141,459
Building Damage | $30.3 Billion | $84.1 Billion
Net Damage Ratio | 2.91% | 5.6%
Total Buildings Cost | $1.04 Trillion | $1.5 Trillion
Detweiler, S.T., and Wein, A.M., eds., 2018, The HayWired earthquake scenario—Engineering implications: U.S. Geological Survey Scientific Investigations Report 2017–5013–I–Q, 429 p., https://doi.org/10.3133/sir20175013v2.
HayWired Scenario: A study lead by USGS, involving approximately 60 partners, to simulate the effects and consequences of a hypothetical, yet scientifically realistic, magnitude M7.0 earthquake on the Hayward fault.

## Slide 20: Anchorage Earthquake Testbed
Tax data for 97,421 buildings/parcels (Municipality of Anchorage appraisal records)
Data was processed to obtain BIM for 84,435 buildings
  78,509 Residential and 7,926 Commercial buildings
Event: Magnitude 7.0 earthquake near Anchorage, Alaska Nov 30th 2018
  12 Recorded ground motions available through CESMD
Anchorage, Alaska Testbed
Parcel level damage
~12,000 buildings in Eagle River
    3,828 red-tagged buildings
    14.5% net buildings loss ratio
Notes: Objective: Demonstrate a computational workflow for a significant simulation that can engage the broad NEHRI community
These testebeds demonstrate the Framework’s connectivity of tools and data by showing how a Regional Earthquake Workflow can analyze each building in the region.
Uses a simplified nonlinear, MDOF model for each building.
Loss estimates are based on a FEMA P-58 methodology.

## Slide 21: Demos

## Slide 22: Questions & Discussion

## Slide 23: Extra Slides

## Slide 24: Research and Educational Tools
SimCenter Research Tools
SimCenter Educational Apps
  Open source software: https://github.com/NHERI-SimCenter

## Slide 25: ECO Activities
Regional Hazard Testbeds
Open-source, Community Driven Software
SimCenter Tool Training Workshop (~June 2019)
Summer Programming Bootcamp (~July 2019)
SimCenter Webinars
Dedicated Slack discussions
Multi-disciplinary REU program
Community Engagement
  https://simcenter.designsafe-ci.org/join-community/